## Slide 1: MASControl3
Its application to energy efficiency calculations and the development of deemed measures
Presented by Maddox Energy Consulting, July 29, 2019

## Slide 2: Safety (SCE)
In the event of an earthquake - go under the table.
When directed, exit the building to designated safety area.
Call 911 – Andres

## Slide 3: Meeting Ground Rules (SCE)
Respect the opinions of all other participants
Skype participants will be muted for most of the training
Submit questions via Skype. As time allows, we will try answering all questions
Improving understanding of MC3 software application for supporting evaluation of EE deemed (DEER and Non-DEER) measures
Training Intent (SCE)

## Slide 4: MASControl Training Agenda
Overview
  Program setup and operation
  Live demo: enable and run an existing measure
DEER Measures
  Basic definitions
  Development environment map and tools
  Live demo: add a new DEER measure
Non-DEER Measures
  Live demo: add a new non-DEER measure
Results review and processing
Working with DEER models in eQuest
Questions and Discussion

## Slide 5: Historical Perspective
Why did we change to MASControl3?
Original MASControl depended on eQuest rulesets and hard-coding
  Complicated structure
  Difficult to expand
MASControl2 moved away from eQuest ruleset, but the alternative BDL ruleset was slow
MASControl3 uses simplified coding, with rules embedded in input via DOE2 macro language
  Relatively simple programming
  Easier to add measures or components

## Slide 6: Installation of MASControl3
Step 1: Unzip files and folders to destination folder
Max length of path to MASControl3 is 39 characters (including “MASControl3”)
Can rename MASControl3 folder to shorter name, if needed
OK to install to more than one place

## Slide 7: Installation of MASControl3
Step 2: Edit INI File – in main MASControl3 folder
Change all path strings to match installation location
Can also change the names of the input and output database files
Step 3: Open program
Double-click on MASControl3.exe in file manager

## Slide 8: Basic Features of MASControl3: Setup
INI file items
Filters on run selections
Database manipulations

## Slide 9: Basic Features of MASControl3: Operations
Select Sim Run List – CSV file with list of runs to perform
Load Sim Run List – gives number of runs and names of runs in status window
Run
Stop (interrupt)
Option to save simulation input and output to InpFiles subfolder
Load only runs for which no results exist in database
Select which results to save to results database
Display loaded list in box below
Show DOS style window when running
If not checked, duplicate result records will be created for any case that was previously run

## Slide 10: Setup Database for a Specific Measure
From the DEER2020.db file, open msrs2proc table in a SQLite browser
  Navicat
  DB Browser for SQLite
Find the desired measure and set “include” to TRUE for that measure
To simplify processing, set undesired measures to FALSE

## Slide 11: Expand Database with New Measure Selection
Step 1: Expand Database
Step 2: Build Full Measure List
Creates All_Measures.csv in \mc3_db\mc3_result\
Contains one line for each valid combination of MeasureID, BldgType, Vintage, Location, and HVAC Type
1
2

## Slide 12: Select Sim Run List – All_Measures.csv
Chooses the full list of enabled measure runs for simulation
Copies contents of All_Measures.csv to Run_Measures.csv

## Slide 13: Load Sim Run List
MASControl3 reads the Run_Measures.csv file in preparation for simulation
Number of simulations shown in Run Status section
Details for all loaded runs are listed in the status window
Unfiltered Run List

## Slide 14: Filtering Run Sets
Add comma separated strings to applicability filters to limit simulations in Loaded Sim Runs
Each box is one independent variable: BldgType, Vintage, Climate, HVAC Type
Order is flexible
For residential, also can limit to specific T-Stat index
TechID filter limits to runs that include a specific TechID: this can be tricky, since it may prevent baseline from running

## Slide 15: Filtering Run Sets – Load Sim Run List
Only runs with independents that match the filter inputs are loaded

## Slide 16: “Hand” Editing Run_Measures.csv
Edit Run_Measures.csv as needed
Then Run “Load Sim Run List”
Gives more flexibility for choosing specific run combinations

## Slide 17: Run Simulations

## Slide 18: Simulation Log File: MASControl3.log
Located in \MASControl\ main folder
Notes any failed runs, and whether failure is in BDL or SIM
File appends for each new simulation set

## Slide 19: Simulation Input/Output Files
INP: DOE-2 input file
BDL: building description language file created when DOE-2 reads the input files: echo of all input code
SIM: text version of simulation output
LRP: non-hourly LOADS simulation results in binary format
SRP: non-hourly HVAC simulation results in binary format
LIN: hourly LOADS simulation results in binary format
SIN: hourly HVAC simulation results in binary format
Binary results files can be programmatically accessed via D2Result.dll

## Slide 20: Basic Definitions – Technology
Technology: an aspect or component of a building that stands by itself
Examples:
  Window unit
  Packaged rooftop AC unit
  Temperature controller
  Flow controller
Each technology is represented by a unique set of Tech Parameters
  Do not use a given Parameter name for two different model properties
    E.g.: Instead of EIR, use Cool_EIR and Heat_EIR
Each Technology definition identified by its unique TechID

## Slide 21: Technology Definition Grey Zones
Can be grey zones in how to define a technology
e.g. the packaged rooftop unit is defined with supply fan, but without the furnace;
  Fan motor efficiency and speed control are part of the DX rooftop unit technology
  Furnace technology with ECM supply fan: uses FanPwrMult parameter to modify the fan motor efficiency
  Economizer is another separate Technology Type

## Slide 22: Technology Type (Tech Type)
Categories of Technologies
  Each Tech Type is defined by a set of Technology Parameters
  Any Technology of that Tech Type has assigned values for those Parameters
E.g.:
  SpltAC_SEER
  PkgAC_SEER
  PkgTermAC
  AirEcono
  ClothesWash

## Slide 23: Prototype Initialization
The Initialized Prototype is a “baseline” model from which measures can be built
Unique for each combination of independent variables:
  Building type
  Building vintage (age)
  Building location (climate zone)
  HVAC system type
Start with building type template
  Contains references to Tech Parameters
Apply a list of Technologies based on independent vars.
Additional non-tech parameters based on independent vars.

## Slide 24: Measure Basics
Measures are defined by technologies
Up to three measure cases (defining technologies):
  Pre = pre-existing building
  Std = standard building; can be energy code or industry standard practice
  Msr = measure case
Simple scenario: Residential blow-in wall insulation retrofit
  Pre technology: no insulation
  Std technology: not applicable
  Msr technology: R-13 fill
Features for more complicated scenarios
  Multiple technologies to comprise a given measure case (MultiTech)
  Selection of technology for a case based on independent variables (VariTech)

## Slide 25: Development Environment
Data Workbooks
SQLite Input Database
Supporting Text Files
SQLite Output Database
MASControl3
Prototype Templates
PostgreSQL ExAnte Database
Simulation Input/Output Files

## Slide 26: Development Environment
Data Workbooks
SQLite Input Database
Supporting Text Files
SQLite Output Database
MASControl3
Prototype Templates
PostgreSQL ExAnte Database
Simulation Input/Output Files

## Slide 27: Model Input File Structure
DOE2 Macro Language is used to reference input within subordinate files
  ##fileprefix [MASControl3 root path]
  ##include [Subfolder\FileName]
Highest level: Master Input File
  Middle level: Building Type + HVAC Template
    Lowest level:
      HVAC Templates (system, zone, and plant)
      Residential space conditions
      Commercial refrigeration

## Slide 28: Highest Level: Master Input File
Created by MASControl3
DOE2 PARAMETER lines:
  Technology parameter assignments
  Non-tech parameter assignments
Macro language lines:
  Fileprefix: to MASControl root folder
  A few key HVAC values
  A few Technology macro variable assignments
  One line to include the building type template

## Slide 29: Middle Level: Building Type + HVAC Template
Design Day
Contains space geometry
  Space locations and dimensions
  Space partitions
  Exterior walls and windows
Contains HVAC configuration
  Grouping of spaces to HVAC systems
  Grouping of systems to plant loops
  Quantity of plant components
  Grouping of systems to VRF outdoor units
  References to HVAC sizing data
##include statements bring in non-geometrical input

## Slide 30: Input File Sample
INPUT ..
##fileprefix C:\DEER\DEER2020\MASControl3\
##set1 IsSizing FALSE
##set1 CoolType DX
##set1 HeatType FURNACE
##set1 EU_HrRepVar 0
##set1 BldgVint 1985
##set1 BldgLoc CZ01
PARAMETER
"AltFactor" = 1.00753 $ IP Non-Tech
"BFMult" = 1 $ IP Tech: RefgChg-NRes-Std
"BldgEconoFlag" = 1 $ IP Non-Tech
"Break_EWSF" = 1 $ IP Non-Tech
"Break_LWSF" = 1.1 $ IP Non-Tech
.
.
.
"HtCap_Sys_T_OfficeSm_N" = -26420.87 $ Sizing
"HtCap_Sys_T_OfficeSm_S" = -69440.28 $ Sizing
"HtCap_Sys_T_OfficeSm_W" = -62139.5 $ Sizing
"HtCap_Sys_T_Restrm_C" = -8828.183 $ Sizing
"HtCap_Sys_T_StorSm_C" = -17385.25 $ Sizing
..
##include Templates\OfL_DX_SZ.inp
END ..
COMPUTE ..
STOP ..
"Entire Year" = RUN-PERIOD-PD
BEGIN-MONTH = 1 BEGIN-DAY = 1
BEGIN-YEAR = 2009 END-MONTH = 12
END-DAY = 31 ND-YEAR = 2009
..
... [ site oriented inputs ]
$ ****************************************************
$ ** Floors / Spaces / Walls / Windows / Doors **
$ ****************************************************
... [ space definitions ]
$ ****************************************************
$ ** HVAC Systems / Zones **
$ ****************************************************
Sys_L_Cordr_C = SYSTEM
TYPE = PVVT
##include IncFiles\SystemDXSZ.inp
CONTROL-ZONE = L_Cordr_CZn
FAN-SCHEDULE = D_OfL_All_Fan_Yr
COOLING-CAPACITY = {#PA("ClCap_Sys_L_Cordr_C")
C-SA-FLOW-BA = {#PA("CSupFlo_Sys_L_Cordr_C")}
C-RTD-FLOW-BA = {#PA("CRtdFlo_Sys_L_Cordr_C")}
..
L_Cordr_CZn = ZONE
TYPE = CONDITIONED
SPACE = L_Cordr_C
##include IncFiles\ZoneDXSZ.inp
COOL-TEMP-SCH = "D_OfL_All_CTemp_Yr"
HEAT-TEMP-SCH = "D_OfL_All_HTemp_Yr"
OA-FLOW/AREA = ( 0.15 )
MIN-FLOW/AREA = 0.15
..
... [ more systems and zones ]
HEAT-SOURCE = {#SIT(#PA("HeatSrc"),"SYSTEM",
"HEAT-SOURCE",#L("TYPE"))}
ZONE-HEAT-SOURCE = NONE
BASEBOARD-SOURCE = NONE
NUMBER-OF-UNITS = 1
MAX-SUPPLY-T = {#PA("MaxSupT_SZ")}
MIN-SUPPLY-T = {#PA("MinSupT")}
COOL-SET-T = { #PA("MinSupT") - 10}
NIGHT-CYCLE-CTRL = CYCLE-ON-ANY
MIN-OA-METHOD = FRAC-OF-HOURLY-FLOW
MAX-OA-METHOD = FRAC-OF-HOURLY-FLOW
$ Economizer
ECONO-LIMIT-T = {#PA("EconoTempLimit")}
... [ 127 lines total ]
DESIGN-HEAT-T = {#PA("DesHeatT")}
DESIGN-COOL-T = {#PA("DesCoolT")}
##if #[HeatType[] EQS HEAT-PUMP]
STARTUP-HEAT-DT = 6
##else
STARTUP-HEAT-DT = 12
##endif
Master Input FIle
C:\MASControl3\InpFiles\
Building/HVAC Template
C:\MASControl3\Templates\
System Include File
C:\MASControl3\IncFiles\
Zone Include File
C:\MASControl3\IncFiles\

## Slide 31: Master Input File Creation
Data Workbooks
SQLite Input Database
Supporting Text Files
SQLite Output Database
MASControl3
Prototype Templates
PostgreSQL ExAnte Database
Simulation Input/Output Files

## Slide 32: Master Input File – Parameter Types
INPUT ..
##fileprefix C:\DEER\DEER2020\MASControl3\
##set1 mCHW_FlowCtrl VarSec $ Msr TechID: ChwFlowCtrlVarTst
##set1 mChlrCap_fT DEFAULT $ IP Tech: ChlrScrW-150to299-0.79kWpTon
##set1 mChlrEIR_fPLR DEFAULT $ IP Tech: ChlrScrW-150to299-0.79kWpTon
PARAMETER
"AltFactor" = 1.00501 $ IP Non-Tech
"BldgEconoFlag" = 1 $ IP Non-Tech
"BlrPrimLp" = BlrPrimLoop $ IP Non-Tech
. . .
"CHW_FlowCtrl" = VarSec $ Msr TechID: ChwFlowCtrlVarTst
"CHW_HdSensLoc" = AT-COILS $ Msr TechID: ChwFlowCtrlVarTst
"CHW_HdSptCtrl" = FIXED $ Msr TechID: ChwFlowCtrlVarTst
. . .
"EconoCtrl" = OA-TEMP $ IP Tech: AirEcono-OATemp
"MaxOAFrac" = 0.85 $ IP Tech: AirEcono-OATemp
"UseEconoVintApplic" = FALSE $ IP Tech: AirEcono-OATemp
. . .
"AltAdjFactor" = 1.005014 $ Sizing
"CAssFlo_L_Break_CZn" = 332.0226 $ Sizing
"CAssFlo_L_Conf_CZn" = 399.6776 $ Sizing
"CAssFlo_L_CopyRm_CZn" = 93.33817 $ Sizing
. . .
..
##include Templates\OfL_CH_MZ.inp
END ..
COMPUTE ..
STOP ..
Macro Variable for Technology defining the measure case
Macro Variables for Technology from Prototype Initialization (IP)
Non-Technology Parameters from Prototype Initialization (IP)
Parameters for Technology defining the measure case
Parameters for Technology from Prototype Initialization (IP)
Parameters from sizing run
A
A
C
B
C
D

## Slide 33: Prototype Initialization – Key Tables

## Slide 34: Non-Technology Parameters for Prototype Initialization
DEER
Independent Variables
Parameter Name
Parameter Value
B

## Slide 35: Technologies for Prototype Initialization
DEER
Independent Variables
Technology Identifier

## Slide 36: Parameters for Technology Initialization
Technology Identifier
Parameter List
If IsMacro = 1, then write as macro variable instead of PARAMETER
A
C

## Slide 37: Workbook-to-Database Data Flow
Data Workbooks
SQLite Input Database
Supporting Text Files
SQLite Output Database
MASControl3
Prototype Templates
PostgreSQL ExAnte Database
Simulation Input/Output Files

## Slide 38: Data Workbooks vs. SQLite Input Database
Data Workbooks
More scattered
  34 workbooks
  ~ 400 worksheets
Organized for data input and review
Intermediate calculations by worksheet formulas
SQLite Input Database
More condensed
  46 tables
  Several sheets/workbook
Organized for efficient operation of MASControl3
Export Tool
Merges worksheet tables

## Slide 39: Data Workbook Folders - Overview
NonTechWorkbooks:
  Build list of non-tech parameters for prototypes
  Build list of TechIDs for prototypes
  Build VariTech lists of TechIDs for measures
TechWorkbooks:
  Contain data for all Technologies
Measures:
  Technology assignments for each measure
  Applicability of measures (Bldg. Type, Location, Climate, HVAC type)
  Normalization units
Geometry: create prototype templates
Tools: Utility workbook to transfer data to SQLite database
LibraryTools: Utilities to create UsrLib.dat file

## Slide 40: Non-Tech Workbooks – Parameter and Tech Lists
DEER
Independent Variables
Prototype Initialization Parameters
Prototype Initialization Technologies
VariTech Measure Technologies

## Slide 41: Tracing Non-Technology Parameters from Database to Source Workbook
DEER
Independent Variables
Parameter Name
Parameter Value
B

## Slide 42: Technology Workbooks
Eight Existing Technology Workbooks – by Category
TechData_Envelope.xlsm
TechData_NonResLtgPlugs.xlsm
TechData_ResApplianceLtg.xlsm
TechData_MscHVAC.xlsm
TechData_PkgHVAC.xlsm
TechData_Plant.xlsm
TechData_DHW.xlsm
TechData_Msc.xlsm

## Slide 43: Technology Workbook Layout
Three key table types in each Tech workbook
Sheet TechTypeDefinitions: one per workbook
  TechTypeID
  List of Parameters for each TechType
Sheet TechData: one or more per workbook (name can vary)
  Unique TechID for each Technology
  Assigned TechTypeID
  Values for each Parameter in the TechType definition
Sheet ParamDefn: one per workbook
  List of all Parameter names used in the workbook
  Can use MacroOrParam column to indicate if DOE2 macro variable
    This column is optional in the table
    Default is PARAMETER only
    B is both PARAMETER and DOE2 macro variable

## Slide 44: Tracing Technology Data – e.g.: COOLING-EIR
Step 1:
Find keyword of interest, and note parameter name
Step 2:
Search for the parameter name from the top of the file: note the TechID
Step 3:
Find the TechID in the Technology table in the database
Step 4:
Note the source workbook:worksheet

## Slide 45: Measure Workbooks – Residential and Non-Residential
Measures sheet:
Unique MeasureID
TechID assignments for each measure case (Pre, Std, Msr)
Applicabilities
  Set valid CZ, vintage, Bldg type, and HVAC type for each measure
  Set AnyBldg to “M” for combined BldgType/HVAC type applicability (tblBldgHvacApplic)
Other
  TStatOptions: Multi for residential and Com for commercial
  EU_HrRepVar: DOE2 hourly report index for end uses to include in hourly reports
  NormUnit: Reference ID for Normalizing Units processing
  SizingSrc: identify which measure case to use for HVAC sizing (default is Pre)

## Slide 46: Tool Workbook: Transfer Data to Database
Setup – enter project folders highlighted yellow:
RepoRoot is the top level of the workbook repository
DefaultTempFolder is a folder where temporary intermediate files are saved
Database folder is the location of the DEER input database

## Slide 47: Geometry Workbooks
File Name | Function
DEER_Geom_tables.xlsm | Data defining DEER commercial building geometry
SpaceData.xlsm | Support tables for commercial building geometry
Gen_Geom.xlsm | Macro for generating commercial building templates
MakeDMo_BB.xlsm | Data and macro for generating mobile home template
MakeMFm_BB.xlsm | Data and macro for generating multifamily template
HowToAddBldgTypes.xlsx | Instructions for adding a new building type to MASControl3

## Slide 48: Commercial Building Geometry
Updated for DEER2020 based on California Commercial Saturation Survey (CSS)
  Same building types,
  Expanded activity areas
Lighting profiles updated based on California EM&V Results
Geometry is abstracted to keep model relatively simple with expanded activity areas

## Slide 49: Abstracted Geometry Viewed in eQuest – Large Office

## Slide 50: Library Tools Workbooks
Tools for generating eQ_Lib.dat / UsrLib.dat
ConstructionLibGen.xlsm: materials & constructions
ProfileLibGen3.xlsm: most schedules
D17_Profiles: newer schedules
HVAC Perf Maps are from TechWorkbooks\TechData_PkgHVAC.xlsm
Make_eQ_Lib.xlsm: build total eQ_Lib.dat or UsrLib.dat from parts

## Slide 51: HVAC Sizing in MASControl3
Where is it Used?
Residential: No
  Sizing is by set based on survey data per home area
Commercial:
  New Vintage: No
  Existing Vintages: Yes
  Separate sizing simulation run for the “sizing baseline”
    For most cases the baseline is the Pre-Existing case
      Which is often the initialized prototype
    For measures where the Pre case is a fault condition, the Msr case is the sizing baseline
      E.g. Refrigerant charge adjustment measures

## Slide 52: Sizing Data in MASControl3 Environment
Geometry Workbooks
Input
Database
Gen_Geom.xlsm
table: SizingID
Data for accessing results in DOE2 binary output files
table: SizingParams
List of components and keywords that need sizing
Output Database
MASControl3
table: sim_sizdat
Sizing results for each simulation
Sizing Runs
Production Runs
table: sim_annual
tables: sim_hourly_wb and sim_hourly_ eu

## Slide 53: Sizing INP Files

## Slide 54: Production INP Files

## Slide 55: How to Add a New DEER Measure of an Existing Measure Type – Example 1: Chiller Efficiency
Add row to Technology table
Add row to DEER_NonRes_Measures.xlsm
  Use existing similar chiller measure as starting point
  Enter alternate TechID in new row
  Change applicabilities, if needed
Import from workbooks to database
  Tech Tables
  Measure Tables
Update msrs2proc
Re-build Database from MASControl3
  Convert Msr Nulls
  Expand Database

## Slide 56: TechData review
Choose a TechType in the drop-down to show Parameter names in row 8
May need to manually change the index in cell E9, based on column C values.

## Slide 57: Add new Technology: TechData_Plant.xlsm
Add row to TechData_Plant.xlsm for new chiller Technology
  Use existing chiller Technology of the same TechType as the source
  Insert new row anywhere
  Enter alternate efficiency in new row
  Make sure TechID is unique and appropriately descriptive
Use similar technology as source row
Create new row as copy of source row and modify parameters as needed

## Slide 58: Measure Workbook Layout (Basics)
Grey section at top used for Export to Database tool (don’t overwrite)
This section is for efficient entry of data to build MeasureID and TechID strings
Each row defines a measure, and must have a unique MeasureID

## Slide 59: Measure Workbook – Bird’s-Eye View
General Information
TechIDs
Single Tech
MultiTech
VariTech
Applicabilities

## Slide 60: Measure Workbook Layout (First Fields)
TStat = Com for NonRes
Multi for Res
“Sizing Baseline”: which measure case to use for HVAC sizing (Default = Pre)
ShowInList not used
Use column from this section when there is one TechID per measure case, and the TechID does not change with Vintatge, CZ, BldgType, or HVAC Type
DOE2 Hrly Rept index for hourly report end use variable
Reference ID for Nomalizing Units Processing
Use this section when there are multiple TechIDs for the “Pre” case. If a TechID does change with Vintatge, CZ, BldgType, or HVAC Type, see next slide for that TechID

## Slide 61: Measure Workbook Layout (MultiTech & VariTech)
MultiTech for Standard case
MultiTech for “Measure” case
Use column(s) here if one TechID per measure case and TechID varies with BldgType, Vintage, etc; the entry is a lookup to the VariTechID field of the VariTech table in the database
MultiTech+VariTech: Use column(s) here if multiple TechIDs per measure case and TechID varies with BldgType, Vintage, etc
If one of the technologies is a VariTech type, then use MuliTech+VariTech below

## Slide 62: Measure Workbook Layout (Applicabilities)
Enables measures for specific combinations of independent variables
For each category, choose either:
  “Any” to include all options for that category
  Specific columns to include a subset of options
Set to “x” or “1” to select
Notes:
Ind and Ag sectors not used for DEER2020
For com lighting, “AnyBldg” = M to filter using sheet BldgTypeHvacApplic

## Slide 63: Add new Chiller Measure: DEER_NonRes_Measures.xlsm
Add row to DEER_NonRes_Measures.xlsm
  Use existing similar chiller measure as starting point
  Enter alternate MsrTechID in new row
  Change applicabilities, if needed
Use similar Measure as source row
New row with measure efficiency

## Slide 64: Rebuild the Database
Run “Transfer Tech Tables”
  Rebuilds the Technology data tables in the input database (TechType, Technology, TechLists, TechID2Param)
Run “Transfer Measure Tables”
  Rebuilds the Measures and MeasureApplicabilities tables in the input database

## Slide 65: NonTechWorkbooks: Msrs2Proc.xlsm
Source Table for msrs2proc table in input database
Table is hand-built in the Msrs2Proc.xlsm file

## Slide 66: Setup to Import Msrs2Proc.xlsm to input database
Go to sheet Tables of ImportTablesToDB.xlsm
Note: this is a good resource to trace the source of miscellaneous tables in the database
Clear “Include” column for all except msrs2proc

## Slide 67: Setup to Import Msrs2Proc to input database
Go to sheet Main of ImportTablesToDB.xlsm
Step 1: Clear “Build Initialization Tables” option
Step 2: Run “Transfer Data Tables” macro

## Slide 68: Prepare MASControl3
Go to Setup Tab
Step 2: Expand Database
Step 1: Convert Measure Table Nulls
Step 3: Build Measure List

## Slide 69: Expand Database – Measures Table Expansion

## Slide 70: Select and Load Sim Run List

## Slide 71: Run Simulations

## Slide 72: Adding New Non-DEER Measures
New Technology Types
  Adding a Tech Type
  Adding PARAMETERS
  Adding Technologies
Measures with MultiTech
Measures with VariTech

## Slide 73: Non-DEER Example #1: HVAC Maintenance/Upgrade
Measure definition:
  Clean coils, pre-existing dirty coil results in:
    Decrease cooling capacity by 20%
    Decrease cooling efficiency by 10%
    Increase fan power by 0.1 W/cfm
  Indoor fan upgrade to ECM: increase motor efficiency
Steps for implementation:
  Check INP templates for existing relevant parameters
  Check if existing TechTypes can handle the new technologies
  Add new TechTypes and/or Technologies
  Add new measures
  Export to database
  Expand database
Note: these values are hypothetical for this example; do not use for actual Non-DEER measures

## Slide 74: HVAC Maint/Upgrade – Check INP Templates
From: \IncFiles\System DXSZ.inp
COOLING-EIR = {#PA("CoolingEIR") * #PA("CoolEirMult")}
SUPPLY-KW/FLOW = { #PA("FanWPerCfm") *
#PA("FanPwrMult")/1000 }
From: \Templates\OfS_DX_SZ.inp
COOLING-CAPACITY = {#PA("ClCap_Sys_T_Hall_W")
* #PA("TotCoolCapMult") }

## Slide 75: Search for Relevant Existing TechTypes – Furnace ECM

## Slide 76: Existing Related Tech Types and Their Parameters

## Slide 77: Prototype Initialization of Related TechTypes
Need to consider whether there is a conflict with parameter values that are set during prototype initialization
Check the related tech types to see how they are initialized
  Furnace Technologies are either “PkgFurn-” or “Furnace-”
  Search for these strings in TechInit table of database
  Then check TechData table for values
PkgFurn-080AFUE is the only TechID found for commercial furnace in the TechInit table.

## Slide 78: FanPwrMult is “Neutral” in Initialized Prototype

## Slide 79: Repeat for RefgChg Tech Type
Check for TechID in Initialized Prototype
RefgChg-NRes-Std is the only TechID found for commercial refrigerant charge in the TechInit table.

## Slide 80: Find RefgChg-NRes-Std in TechData Table
The TotCoolCapMult and CoolEirMult parameters are both “Neutral” in the Initialized Prototype, with values of 1.0.
If the values had been other than 1.0, then measure technologies would need to account for those baseline values.

## Slide 81: Technologies for the New Measure - ECM
For the fan ECM, the existing TechType and Technologies will work

## Slide 82: Fan Power Effect of Dirty Coil
Add new Tech parameter “FanPwrOffset” to DXSZ template to account for pressure loss due to dirty fan
From: \IncFiles\SystemDXSZ.inp
COOLING-EIR = {#PA("CoolingEIR") * #PA("CoolEirMult")}
SUPPLY-KW/FLOW = { #PA("FanWPerCfm") * #PA("FanPwrMult")/1000
+ #PA(“FanPwrOffset”)/1000 }

## Slide 83: New Parameter for TechType
Add new FanPwrOffset parameter to TechTypeDefinitions for RefgChg Tech Type

## Slide 84: New Parameter in ParamDefn
Insert row and enter ID, Display and Description for new parameter

## Slide 85: Technologies for the New Measure – Coil Cleaning
Values need to be added to the FanPwrOffset parameter for the existing RefgChg technologies (value of “0” is neutral)
For the coil cleaning measure, use the RefgChg TechType but create new Technologies

## Slide 86: Add New Measure Entry to DEER_NonRes_Measures.xlsm
Since measure is MultiTech, these cells are left blank
These are the TechIDs for the two baseline technologies
These are unique identifiers for the MultiTechID field of the TechLists table in the database
Note: two measures can use the same MultiTechID, but the TechIDs must be the same for both
These are the TechIDs for the two measure technologies

## Slide 87: Potential Pitfall with Measure Setup - TechID Typos
If there is a typo in the TechID entry in the Measures table
  Technology initialization will fail
  Simulation will run
  There will be no error message
Check simulation to ensure that TechIDs are initialized
Future version of tool should include a check on TechID validity

## Slide 88: Rebuild the Database
Setup Msrs2Proc.xlsm and run “Transfer Data Tables”
Run “Transfer Tech Tables”
Run “Transfer Measure Tables”

## Slide 89: MultiTech in Input Database

## Slide 90: Non-DEER Example #1 Wrap-Up
Same steps as for DEER Measure Example
Expand Database
Build Measure List
Load Measure List
Run Simulations

## Slide 91: Simulations for Example #1
Note sizing is done with measure technology
Subsequent Tech Run is the Pre case

## Slide 92: Non-DEER Example #2: MultiTech with VariTech
Measure definition – modification of Example #1:
  Clean coils, pre-existing dirty coil results in:
    Decrease cooling capacity by 20%
    Decrease cooling efficiency by 10%
    Increase fan power by 0.1 W/cfm
  Indoor fan upgrade to ECM: increase motor efficiency
    Pre-existing building has ECM for vintages 2017 and later
Steps for implementation (building from Example #1):
  Add VariTech data to NonTech workbooks
  Same Technologies as Example #1
  Enter VariTechID into Measures workbook
  Export to database
  Expand database

## Slide 93: Add VariTech Data to NonTech Workbooks
New column added for VariTech

## Slide 94: Make Sure VariTechID is Not Already In Use

## Slide 95: VariTech in DEER_NonRes_Measures.xlsm

## Slide 96: Non-DEER Example #2 Wrap-Up
Same as for previous examples
Expand Database
Build Measure List
Load Measure List
Run Simulations

## Slide 97: Expand Database – Initialization Tables
To include new VariTech data, need to rebuild initialization tables
Also include new measure in msrs2proc

## Slide 98: Transfer To DB
Transfer Data Tables
Transfer Measure Tables
Don’t need tech tables this time

## Slide 99: VariTech Simulations
Tech Run is the Pre case – this is the MultiTechID
Sizing Run is the Msr case – this is the MultiTechID

## Slide 100: Example #1 vs. Example #2 in Results Database
For the VariTech (VT) measure, the Pre case includes the EC motor, so fan penalty is only due to dirty coil.
For the VariTech (VT) measure, the fan penalty is due to both dirty coil and non-EC motor

## Slide 101: Tracing VariTech Data from DB to Workbooks

## Slide 102: MASControl3 Results
MASControl3 Output Database
  Automatically populated by MASControl3
  SQLite Format
  Annual and hourly results for each technology
  Unweighted
Post-Processed Database
  Requires setup and execution of post-processing queries
  CPUC version is PostgreSQL
  Measure impacts (difference between baseline and measure technology)
  Weighted averages (vintage, location, etc.)

## Slide 103: SQLite Results Database – sim_annual
IP: Technology = initialized prototype
Each row contains results from one Technology simulation
“therm” columns are actually Btu

## Slide 104: SQLite Results Database – sfm_annual
1 = single story house
2 = two story house
1 & 2 merged in post-processing
For SFm,“therm” columns are really therms

## Slide 105: SQLite Results Database - hourly
One 24 hour day per row
365 rows per Technology run

## Slide 106: Post-Processing Calculations
Weighting of Results
  Existing Building = Average of Vintages
  Location/ PA Result = Average of Climate Zone Results
  HVAC Avg. Result = Averages of HVAC Types
  Residential Thermostat = Average of 5 scenarios
  Building Type = Average of Building Types in Sector
Calculation of Peak Period Demand
Calculation of Impacts
  Above Pre = Pre Technology – Msr Technology
  Above Std = Std Technology – Msr Technology

## Slide 107: Post-Processing Resources
Files: MC3_Post_Processing.zip
  Instructions: MASControl3 Processing Guide.pdf
  Queries
    Setup (SupportTables)
    Residential
    Commercial
PostgreSQL
  pgAdmin4: Freeware to create and maintain PostgreSQL database

## Slide 108: Post-Processing Steps
Setup Database
  Create Database
  Import Technology run result data
  Import support tables
Run Queries
  Commercial
    P1: Create peak period values
    P2: Calculate measure impacts
    P3 to P8: Calculate weighted averages
    P9: Format results for Ex-Ante tables
  Residential
    R1 to R4: Weighted averages of five thermostats
    P1 to P9: Same logic as commercial, but these are different query files

## Slide 109: Post-Processing Database Type
DEER uses PostgreSQL database
  More complicated to set up than SQLite
  Need to export results from MASControl3 results database
  Can use DEER queries directly
  Can be shared across internet
Could also use SQLite (or other) format
  Can be simpler setup
  Easier to transfer existing MASControl SQLite results tables
  Need to modify DEER queries to work in SQLite
  Share DB by sending file

## Slide 110: PostgreSQL – Export from SQLite
Dump SQL creates a query file which will re-create the table when run from the target database

## Slide 111: Import to PostgreSQL sim_annual
PRAGMA foreign_keys = OFF;
DROP TABLE IF EXISTS "main"."sim_annual";
CREATE TABLE "sim_annual" (
"TechID" TEXT(255),
"SizingID" TEXT(255),
"BldgType" TEXT(255),
"BldgVint" TEXT(255),
"BldgLoc" TEXT(255),
"BldgHVAC" TEXT(255),
"tstat" TEXT(255),
"normunit" TEXT(255),
"numunits" REAL(24),
"measarea" REAL(24),
"kwh_tot" REAL(24),
"kwh_ltg" REAL(24),
. . .
"kwh_venthtg" REAL(24),
"kwh_ventclg" REAL(24),
"kwh_refg" REAL(24),
"kwh_hpsup" REAL(24),
"kwh_shw" REAL(24),
"kwh_ext" REAL(24),
"thm_tot" REAL(24),
"thm_equip" REAL(24),
"thm_htg" REAL(24),
"thm_shw" REAL(24),
"deskw_ltg" REAL(24),
"deskw_equ" REAL(24),
"lastmod" TEXT(6)
);
-- ----------------------------
-- Records of sim_annual
-- ----------------------------
INSERT INTO "main"."sim_annual" VALUES ('IP', 'None’,...
SET search_path TO reshvac;
DROP TABLE IF EXISTS "sim_annual";
CREATE TABLE "sim_annual" (
"TechID" varchar(255) NOT NULL,
"SizingID" varchar(255) NOT NULL,
"BldgType" varchar(255) NOT NULL,
"BldgVint" varchar(255) NOT NULL,
"BldgLoc" varchar(255) NOT NULL,
"BldgHVAC" varchar(255) NOT NULL,
"tstat" varchar(255) NOT NULL,
"normunit" varchar(255),
"numunits" numeric,
"measarea" numeric,
"kwh_tot" numeric,
"kwh_ltg" numeric,
. . .
"kwh_venthtg" numeric,
"kwh_ventclg" numeric,
"kwh_refg" numeric,
"kwh_hpsup" numeric,
"kwh_shw" numeric,
"kwh_ext" numeric,
"thm_tot" numeric,
"thm_equip" numeric,
"thm_htg" numeric,
"thm_shw" numeric,
"deskw_ltg" numeric,
"deskw_equ" numeric,
"lastmod" varchar(255),
CONSTRAINT "sim_annual_pkey" PRIMARY KEY ("TechID", "BldgType", "BldgVint", "BldgLoc", "BldgHVAC", "tstat")
);
-- ----------------------------
-- Records of sim_annual
-- ----------------------------
INSERT INTO "sim_annual" VALUES ('IP', 'None’,...
Format as exported from SQLite
Format needed for import to PostgreSQL
“reshvac” = name of Schema in PostgreSQL database
Identify fields to be primary keys

## Slide 112: P# and R# Queries
-- Create the simulation peak period demand value table from the hourly data table.
-- Whole Building kw: PeakDay 2 - 5 (previous DEER), 4 - 9 (DEER2020) on 3-day Heatwave
-- Time Estimate: 600 seconds
SET search_path TO "MC_results_database";
DROP TABLE IF EXISTS sim_peakper;
CREATE TABLE sim_peakper AS
SELECT "TechID","SizingID","BldgType","BldgVint",sim_hourly_wb_wtd."BldgLoc" as "BldgLoc","BldgHVAC",
round(((Sum(hr14)+Sum(hr15)+Sum(hr16))/9)::NUMERIC(15,3),3) as bldg_kw25,
round(((Sum(hr16)+Sum(hr17)+Sum(hr18)+Sum(hr19)+Sum(hr20))/15)::NUMERIC(15,3),3) as bldg_kw49
FROM sim_hourly_wb_wtd
JOIN peakperspec ON sim_hourly_wb_wtd."BldgLoc" = peakperspec."BldgLoc"
WHERE ((daynum::smallint = "PkDay"::smallint) or (daynum::smallint = "PkDay"::SMALLINT+1) or (daynum::smallint = "PkDay"::SMALLINT+2))-- and enduse::SMALLINT = 20
GROUP BY "TechID","SizingID","BldgType","BldgVint",sim_hourly_wb_wtd."BldgLoc","BldgHVAC";
Example: Residential P1-Create-sim_peakper.sql
“MC_results_database” = name of Schema in PostgreSQL database

## Slide 113: Normalizing Units
For each measure run, normalizing units are calculated by MASControl3

## Slide 114: NormUnitDef Table in Input Database
NormUnit assigned in Measures table
NormSrc:
  NUfromTable: lookup from table NormUnitVal
  NUfromSizDat: lookup from sizing data
  None: numunits = 1

## Slide 115: Normalizing Units – Lookup from NormUnitVal table
e.g. for SFm, if NormUnit in measure table is specified as “Household”, then numunits value is 2

## Slide 116: Normalizing Units – Lookup from sim_sizdat table
Lookup is filtered based on values in NormUnitDef and SizingParams as shown here

## Slide 117: Adding a New Norm Unit Type – NormUnitDef table
Example Scenario: New measure type for variable speed chilled water pumps
In Measures table set NormUnit to ChwPumpHP
In NormUnitDef table, add a record with same NormUnit
  Divisor applies the motor efficiency and unit conversion to the simulation motor kW value
  In this case Keyword is not a DOE2 keyword, but a string that relates to the other relevant database tables
  Note: NormUnitDef table does not have a non-Tech workbook source

## Slide 118: Adding a New Norm Unit Type – SizingID table
In the SizingID table add one record
  This tells MASControl3 where to find the pump kW in the binary simulation output file
  The EntryID is found in the NHRList.txt file
  Note: the source for the SizingID table is the non-tech workbook DEER_SizingID_Tables.xlsm

## Slide 119: Adding a New Norm Unit Type – SizingParams table
In SizingParams table add one record per building type to identify the name of the pump (PrimKey) for which sizing is needed
Note: the SizingParams table is created by the Geometry workbooks (Gen_Geom.xlsm)

## Slide 120: Adding a New Norm Unit Type – sim_sizdat table
sim_sizdat is populated by MASControl3
NormUnits value is ParamVal / Divisor or 17.008/1.25

## Slide 121: Importing to eQuest – DOE-2.3
Install latest eQuest from DOE2.com: eQUEST_3-65_Build7175_2018-10-04.msi
Setup eQuest for DOE2.3
  Open \Documents\eQUEST 3-65-7175 Data\eQuest.ini
  Change line #38 to: DOE2Version=2
Copy USRLib.dat from: MASControl3\DOE2\exe\DOE23\USRLib.dat and use it to replace \Documents\eQUEST 3-65-7175 Data\DOE23\eQ_Lib.DAT

## Slide 122: Importing to eQuest – DOE-2.2R
Install latest eQuest from DOE2.com (same as for DOE-2.3 in previous slide): eQUEST_3-65_Build7175_2018-10-04.msi
Copy usrlib.dat from: MASControl3\DOE2\exe\DOE22R\usrlib.dat and use it to replace both: \Documents\eQUEST 3-65-7175 Data\DOE2R\eQ_Lib.DAT AND \Documents\eQUEST 3-65-7175 Data\DOE2R\USRLib.DAT
To start eQuest for DOE-2.2R, run the program:
  C:\Program Files (x86)\eQUEST 3-65-7175\eQRefrig.exe
  Do not need to change eQuest.ini

## Slide 123: Open As INP

## Slide 124: Open as PD2
Documents\eQUEST 3-65 D23 Projects\MC3_FileOpen\
OfS-CZ06-2017-cDXGF-IP-Sizing0.pd2
Proj "OfS-CZ06-2017-cDXGF-IP-Sizing"
ProgramVersion = "eQUEST 3.65.7175"
ProductCode = "eQUEST"
WeatherFile = "CZ2\CZ06.bin"
CreateDate = 1563452883
ModDate = 1563452883
LibraryFile = "eQ_Lib.dat"
InterfaceMode = 1
AllowWizard = 0
InputUnitsType = "English"
OutputUnitsType = "English"
..
END_OF_FILE
Copy INP to eQuest Project folder
Create simple PD2
Open PD2 from eQuest

## Slide 125: Macros Resolved after Saving from eQuest

## Slide 126: eQuest Batch Processing
Can be executed on INP files that contain macro language
Need to have hand-built PD2 file for each INP
Macros are resolved for each simulation

## Slide 127: Submitted Questions
Why is New vintage only generating “sizing” INP files for our HVAC measures? [Can’t evaluate without more information.]
Grocery and refrigerated warehouse won’t open in eQuest. [See presentation.]
Is there a way to limit simulations to only the baseline case? [Not with current tools.]
Explanation for measures having up to 3 tech runs. [See presentation.]
Output file types. [See presentation.]
DOE2 Keyword changes – changes on keywords between versions of MASControl (EIR vs CoolingEIR).

## Slide 128: Submitted Questions
Clarify normalizing units. [See presentation.]
Role (if any) of “BDL rules” in MASControl3? [Not used.]
MASControl3 sometimes crashes when hourly results file has more columns than standard. [Default results queries are not designed to handle them. Source code is available from CPUC through end-user licensing agreement.]
Library section sources? [Some from old DOE2 Lib.dat. See presentation for others.]
Can refrigeration measures be run in MASControl3? [Yes.]

## Slide 129: Discussion